## Slide 1: EEG Multimodal

## Slide 2: Multimodal Models https://www.nature.com/articles/s41746-020-00341-z

## Slide 3: Multimodal Models https://www.nature.com/articles/s41746-020-00341-z
IN THIS PROJECT

## Slide 4: EEG Models

## Slide 5: EEG signal analysis using deep learning: A systematic literature review https://ieeexplore.ieee.org/abstract/document/9626707

## Slide 6: Deep Convolutional Neural Network Model for Automated Diagnosis of Schizophrenia Using EEG Signals https://www.mdpi.com/2076-3417/9/14/2870
Task: Binary classification (yes/no Schizophrenia)
Results:
  accuracy = 98.07%
  sensitivity (recall) = 97.32%
  specificity = 98.17%
  positive predictive value = 98.45%
EEG signals
  19 channels, sampling frequency 250Hz
  Z-score normalization
  Signals were segmented
    Each segment consisted of a 25 s (6250 sample) window length
    Each segment consisted of 6250 × 19 sampling points
    A total of 1142 EEG segments were used

## Slide 7
Model layers
convolution
batch normalization
max pooling
average pooling
global average pooling
dropout (p=0.5)
Leaky Relu
Softmax
Model training
Adam
learning rate = 0.001
50-70 epochs
k-fold cross-validation

## Slide 9: A deep convolutional neural network model for automated identification of abnormal EEG signals https://link.springer.com/article/10.1007/s00521-018-3889-z
Task: Binary classification (abnormal/normal signal)
Results:
  classification error rate of 20.66% in classifying the normal and abnormal EEG signals.
EEG signals
  1 channel (T5-O1 and F4-C4), sampling frequency 250 Hz
  The first 60s sections of each EEG record were used (15000 data points)
  2 steps normalization
    the signals are normalized to 0 - 1.
    the signals were standardized by removing the mean and scaling to unit variance

## Slide 14: Automated EEG-based screening of depression using deep convolutional neural network https://www.sciencedirect.com/science/article/abs/pii/S0169260718301494?via%3Dihub
Task: Binary classification (yes/no depression)
Results
  accuracies of 93.5% and 96.0% using EEG signals from the left and right hemisphere, respectively.
EEG signals
  recording time = 5 minutes
  sampling rate = 256 Hz
  notch filter of 50 Hz to eliminate power line interference
  Z-score normalization to overcome the amplitude scaling problem
  segmentation
    Each record consisting of 2,000 sampling points (7.8s)

## Slide 15
Model layers
convolution
batch normalization
max pooling
Dropout (only FC layers)
Leaky Relu
Softmax
Model training
batch size = 5
Adam
  β1 = 0.9
  β2 = 0.999
  lambda = 0.2
learning rate = 0.0001
k-fold cross-validation

## Slide 17: Deep convolutional neural network for the automated detection and diagnosis of seizure using EEG signals https://www.sciencedirect.com/science/article/abs/pii/S0010482517303153?via%3Dihub
Task: Binary classification (yes/no seizure)
Results
  88.67% accuracy
  95.00% sensitivity
  90.00% specificity
EEG signals
  Single-channel 300 EEG signals
  duration of 23.6 seconds
  Z-score normalization

## Slide 20: A Novel Convolutional Neural Network Classification Approach of Motor-Imagery EEG Recording Based on Deep Learning https://www.mdpi.com/2076-3417/11/21/9948
Task: Multiclass classification (Left hand/Right Hand/Tongue/Feet)
Results
  88.67% accuracy
  95.00% sensitivity
  90.00% specificity
EEG signals
  recording time = 5 min, sampling frequency = 250 Hz
  bandpass filter (7–30 Hz)
  50Hz notch filter to remove power-line noise
  Extract frequency characteristics using Wavelet Packet Decomposition (WPD)
    decomposition of the low-freq part and the high-freq part of the signal
  Extract spatial characteristics using Common Spatial Pattern (CSP)

## Slide 22
CNN 1
CNN+LSTM (CNN 2)
Modified Merged CNNs
Merged CNNs

## Slide 23
simple CNN models perform better
addition of the LSTM layers in the CNN model does not improve model

## Slide 24: EEG Classification of Normal and Alcoholic by Deep Learning https://pubmed.ncbi.nlm.nih.gov/35741663/
Task: Binary classification (Normal/Alcoholic)
Results
  Accuracy = 99.32%
  Precision = 99.01%
  Recall = 98.87%
  F1-score = 98.93%
EEG signals
  64 channels
  Sampling frequency = 256Hz
  standard deviation standardization

## Slide 25
Data preprocessing (normalization)
discrete wavelet transform → extract time-frequency domain features
CNN + Bi-LSTM → extract spatiotemporal features
  CNN  extract time-series patterns
  Bi-LSTM  use previous/following time-series patterns to calculate output
classification

## Slide 26
4 convolution layers (extract features)
1D conv
Size = 3x1
Stride = 1
ReLU
2 max pooling layers (reduce dimensionality)
Size = 2
Stride = 2
4 fully connected layers
1 sigmoid output layer.

## Slide 28: Scalp EEG-Based Pain Detection Using Convolutional Neural Network https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=9696316
Task: Binary classification (Non-Pain/Pain)
Results
  average AUC = 0.83
EEG signals
  32 channels, sampling frequency = 250 Hz
  band-pass filter (0.5Hz, 100Hz)
  50Hz notch filter
  Independent Component Analysis (ICA) for artifact removal
  Segmentation
  cropped into segments using a 5s sliding window with 4s overlap (5 seconds length segments)
    1 segment = 1250 data points (250 x 5)

## Slide 30
Grid search  Optimizer: SGD, activation function: ELU
convolutional layers (temporal filters, spatial filters)
  Key point: EEG signals have temporal and spatial information
After each max-pooling layer, a 30% dropout is used to avoid overfitting

## Slide 32: EEGNet: A Compact Convolutional Network for EEG-based Brain-Computer Interfaces https://arxiv.org/abs/1611.08024
Task: Multiclass classification
EEG signals
  C channels, T time samples
  band-pass filter (1Hz, 40Hz)
  downsampling to 128 Hz  sampling frequency = 128Hz

## Slide 33
Training
Adam optimizer (with default parameters)
500 training epochs
Model specs (EEGNet-F1,D)
First convolutions = Temporal filter + spatial filter
Temporal filter kernel size = (1, fs/2)
  Setting the length of the temporal kernel at half the sampling rate allows for capturing frequency information at 2Hz and above.
spatial filter kernel size = (C, 1)